## Slide 1: 03/04/2025
Hybrid Homomorphic Encryption Resistance to Side-channel Attacks
Pierugo Pace (NAGRA Kudelski Group / EPFL), Hervé Pelletier (NAGRA Kudelski Group), Serge Vaudenay (EPFL)
CASCADE Conference

## Slide 2: Table of Contents
Context
Attack results
Defense and its effectiveness
Deep Learning to bypass countermeasures
Conclusion and future work

## Slide 3: Context
Cloud services become more popular
  Privacy concerns as data is processed unencrypted
Idea: process data that stays encrypted
Fully Homomorphic Encryption [1]:
  Confidentiality
Actual encryption is expensive
  Especially for IoT
→ Hybrid Homomorphic Encryption [2]
[1] https://www.cs.cmu.edu/~odonnell/hits09/gentry-homomorphic-encryption.pdf
[2] https://eprint.iacr.org/2011/405.pdf

## Slide 4: Hybrid Homomorphic Encryption
CONTEXT
,
Legend:
  :
  :
SK

## Slide 5: Hybrid Homomorphic Encryption
Same guarantees as Fully Homomorphic Encryption
  Confidentiality
  Computation on encrypted data
Smaller ciphertexts → less bandwidth used
Overhead shifted to the server
Perfect for IoT !
Symmetric decryption must be efficient homomorphically
  → Elisabeth-b4 !
CONTEXT

## Slide 6: Elisabeth-b4 [3]
Symmetric stream cipher operating in
Designed to be easily decryptable homomorphically
Stream:
  512-nibble key
  Random whitened subset (RWS) → 98-nibble keyround
  Keyround divided in 14 blocks of size 7 and function is applied to each of them
[3] https://eprint.iacr.org/2023/1895.pdf

## Slide 7: Setup
ATTACKS
(Kudelski IoT Security Evaluations Lab)

## Slide 8: Traces collection
@500Ms/s → 80 000 timepoints per trace
ATTACKS

## Slide 9: Correlation Power Analysis [4]
ATTACKS
Additions and S-boxes
  Efficiently decryptable homomorphically
Recover element by element
Revert RWS thanks to public IV
Requires 35 000 traces to retrieve the entire key
  Only targeting one of the S-boxes’ output
  With 4-bit hypotheses on a 32-bit processor
[4] https://iacr.org/archive/ches2004/31560016/31560016.pdf

## Slide 10: Correlation Power Analysis [4]
ATTACKS
[4] https://iacr.org/archive/ches2004/31560016/31560016.pdf
Maximum correlation factor across the entire trace.
Real key element is 1.

## Slide 11: Templates (Multivariate Gaussian) [5]
PROFILING ATTACKS
Train size Test size | 500 | 750 | 1 500 | 2 500
60 000 | 94.84 ± 1.96% | 98.12 ± 1.22% | 99.92 ± 0.10% | 100.00 ± 0.00%
100 000 | 98.01 ± 1.04% | 99.53 ± 0.40% | 100.00 ± 0.00% | 100.00 ± 0.00%
Templates key recovery rate (5-fold validated) for different profiling and extraction sizes
variables to predict
Feature selection through PoIs (SOST [6])
Assume traces follow a multivariate Gaussian distribution
[5] https://link.springer.com/content/pdf/10.1007/3-540-36400-5_3.pdf
[6] https://eprint.iacr.org/2014/332.pdf

## Slide 12: Countermeasures: Leakage comparison and CPA
Masking [7] and Shuffling [8]
T-test to find leakage points (TVLA [9])
Eliminated first-order leakage
CPA mitigated with masking shares changing every trace
DEFENSES
[7] https://link.springer.com/content/pdf/10.1007/3-540-48059-5_15.pdf
[8] https://link.springer.com/content/pdf/10.1007/978-3-642-34961-4_44.pdf
[9] https://csrc.nist.gov/csrc/media/events/non-invasive-attack-testing-workshop/documents/08_goodwill.pdf

## Slide 13: Templates
Shuffling
  → 16 Random Start Indices
Masking:
  98 values each with 2 shares
  Separately predicted during RWS and
  → mask shares
Total of 408 variables, compared to 98 without countermeasures
Templates: 20% recovery with 250’000 extraction traces: too complex
BYPASSING DEFENSES

## Slide 14: Deep Learning
Similar countermeasures attacked by DL in a 2021 work [10]
A few attempts:
  20 billion parameters with the same architecture:
    Too many parameters to train
  Reduction to 188 million:
    Wavelet transform [11], focus on leakage regions, reduce number of intermediary nodes
    Performance not satisfactory
  Split the trace and train 20 smaller independent models on subwindows of the trace.
    Easier to train due to less parameters per model
    Use multiple GPUs
BYPASSING DEFENSES
[10] https://eprint.iacr.org/2021/592.pdf
[11] https://ieeexplore.ieee.org/document/6472489

## Slide 15: Defenses impact
BYPASSING DEFENSES
Overall attack results with countermeasures enabled.
Method | # Profiling | # Extraction | (%) | (%) | (%) | (%) | (%) | Key recovery (%)
CPA | mitigated | mitigated | - | - | - | - | - | mitigated
Templates | 675,000 | 250,000 | 69.96 | 65.92 | 58.01 | 7.71 | 7.37 | 20.7
Single NN | 675,000 | 250,000 | 74.12 | 58.93 | 37.71 | 6.85 | 6.98 | 12.5
20 NNs | 675,000 | 250,000 | 99.35 | 75.11 | 60.23 | 9.58 | 8.44 | 100
Baseline | 0 | 0 | 1.02 | 7.14 | 14.29 | 6.25 | 6.25 | 6.25
Method | # Profiling | # Extraction |  |  |  |  |  | Key recovery (%)
CPA | mitigated | mitigated | - | - | - | - | - | mitigated
Templates | 675,000 | 250,000 | 69.96 | 65.92 | 58.01 | 7.71 | 7.37 | 20.7
Single NN | 675,000 | 250,000 | 74.12 | 58.93 | 37.71 | 6.85 | 6.98 | 12.5
20 NNs | 675,000 | 250,000 | 99.35 | 75.11 | 60.23 | 9.58 | 8.44 | 100
Baseline | 0 | 0 | 1.02 | 7.14 | 14.29 | 6.25 | 6.25 | 6.25

## Slide 16: Conclusion & Future Work
Side-channel analysis on a new and relevant technology – Hybrid HE
Very feasible to retrieve the whole key without protection
  Even with 4-bit leakage on a 32-bit processor
Masking and shuffling increase the attack complexity
  250x more traces, need to train several DL models
Future work:
  Adapt the architecture of the cipher to eliminate some leaking regions
  Analyse how other HHE schemes (Pasta, HERA, Rubato) are affected by the same attacks

## Slide 17: Feature Reduction [13]
Sum Of Squared pairwise T-differences (SOST)
Measure of discriminatory potential for each timepoint
Choose the timepoints of the N highest values
  Automatic process to capture the maximal information from the traces
Repeat for each of the 98 key values
PROFILING ATTACKS
[13] https://eprint.iacr.org/2014/332.pdf

## Slide 18: Feature Reduction [13]
PROFILING ATTACKS
[13] https://eprint.iacr.org/2014/332.pdf
Example of SOST functions on top of a trace.

## Slide 19
Initial neural network architecture
128
ResNet
9 residual blocks
12,150
3,072
PoIs of 2nd order Haar transform of whole trace
16
Softmax
128
ReLU
128
BN
16
128
16
Softmax
128
ReLU
128
BN
16
Dense
Dense
Dense
Dense
···
512
7
Softmax
512
ReLU
512
BN
7
Dense
Dense
196
512
7
Softmax
512
ReLU
512
BN
7
Dense
Dense
···
14
Dense
128
Dense
16
Softmax
128
ReLU
128
BN
16
128
16
Softmax
128
ReLU
128
BN
16
···
Dense
Dense
196
512
98
Softmax
512
ReLU
512
BN
98
Dense
Dense
512
14
Softmax
512
ReLU
512
BN
14
Dense
Dense

## Slide 20
ResNet
10 residual blocks
19850
2304
RWS
Dense
1024
Dense
98
Softmax
1024
ReLU
1024
BN
98
RWS perm (11,497,410 params)
700
2816
’s PoIs
1024
14
Softmax
1024
ReLU
1024
BN
14
ResNet
5 residual blocks
Dense
Dense
Round perm (4,389,998 params)
Our modular network architectures (1/2)

## Slide 21
ResNet
8 residual blocks
4875
2304
¼ RWS
Dense
512
Dense
16
Softmax
512
ReLU
512
BN
16
¼ RWS masks (63,107,168 params)
512
16
Softmax
512
ReLU
512
BN
16
···
Dense
Dense
48
ResNet
6 residual blocks
1400
2816
Round
512
16
Softmax
512
ReLU
512
BN
16
Round masks and perms (26,213,447 params)
512
16
Softmax
512
ReLU
512
BN
16
Dense
Dense
Dense
Dense
···
1024
7
Softmax
1024
ReLU
1024
BN
7
Dense
Dense
14
Our modular network architectures (2/2)

## Slide 22: Guessing entropies
PROFILING ATTACKS
Templates – without countermeasures
20 NNs – with countermeasures

## Slide 23: An innovative countermeasure
Two major observations of the Deep Learning attack
  Training and inference done on different devices
  Too complex without reducing input size and focusing on leaking regions
Goal: change data distribution between training and inference phases
Inject unpredictable delays consistent to each device
  Harnessing a secret specific to the device
Delays also change every time the key changes
  Complexify attacker that can directly train on the target
DEFENSES

## Slide 24: Effects on leakage regions
AN INNOVATIVE COUNTERMEASURE